## Slide 1: Introduction of a priori domain knowledge in function approximation using shape-constraint P-splines
Jakob Weber

## Slide 2: Overview - Agenda
Problem formulation & motivation
Linear models, Regularization & Penalized Least-Squares
B-splines & P-splines
Shape-constraint P-splines
Experiments
Summary & Questions

## Slide 3: Problem formulation & motivation
Massive increase of process data in the last years
Used to enhance process control concepts based on mathematical models
White-box (first principles) vs. black-box (data)
Specific a priori domain knowledge (AD) often available
  Physics based
  Heuristics
Incorporate the AD into the mathematical model  grey-box model
   Algorithm for efficient, multi-dimensional static function approximation using a priori domain knowledge

## Slide 4: Process Model
Hybrid
Physics-based
Data-driven
Process Model
Data
Physical Knowledge
Prediction
Notes: White Box ->Physics based
Black Box -> Data driven
Grey Box -> Hybrid Modeling

## Slide 5: Process Model
Hybrid
Physics-based
Data-driven
Process Model
Data
Physical Knowledge
Prediction
First-principle modeling
ODEs & PDEs
Constraints
Linear Models
Neural Networks
Non-parametric Models
Gaussian Process Regression

## Slide 6: Process Model
Hybrid
Physics-based
Data-driven
Process Model
Data
Physical Knowledge
Prediction
First-principle modeling
ODEs & PDEs
Constraints
Linear Models
Neural Networks
Non-parametric Models
Gaussian Process Regression
   Algorithm for efficient, multi-dimensional static function approximation using a priori domain knowledge

## Slide 7: Linear models
Model the data assuming additive noise
Unknown function is a linear combination of the inputs
And with the complete data
Notes: How do I get the red line?

## Slide 8: Least Squares Formulation
Linear model
Least squares loss function
Least squares estimate
Notes: If we now have the situation of having a large number of features (aka. Predictors, variables), especially a larger number of features than that of data points, we can use the concepts of regularization to restrict the parameter space

## Slide 9: Regularization & Penalized least squares
Restrict the parameter space by adding a penalty term to the loss function
depending on the complexity of the model
with
and
leading to
Question: How do we cope with non-linear behavior in the data?
Notes: -e.g. Ridge Regression for K = Identity

## Slide 10: B-splines
Lin. comb. of B-spline basis functions of order defined on a sequence of knots
Each basis function is a piecewise polynomial and defined recursively as

## Slide 11: B-spline & Parameter estimation
Using data
we can formulate a model with known structure
and use the least squares formulation to estimate the parameters
With the B-spline basis matrix

## Slide 12: B-splines for = 10
Notes: d = 10 basis functions each
100 datapoints x = [0, 2*pi]
y = 1.5 sin(x) + x

## Slide 13: B-splines for = 25
Notes: d = 10 basis functions each
100 datapoints x = [0, 2*pi]
y = 1.5 sin(x) + x

## Slide 14: B-spline
To define a B-spline, we need
  Order
  Number of basis functions
  Knot sequence
Basic properties of B-spline basis functions or order
  Consist of polynomial pieces of degree
  Derivatives up to order are continuous
  Is nonzero on a domain spanned by knots (locality feature)
  At every given , only B-spline basis functions are nonzero

## Slide 15: B-spline basis matrix
Notes: B-spline basis matrices for l=0,1,2,3 and d=10 and n=100
We see that with increasing degree l, the area of influence for each BF increases, but we also see the LOCALITY FEATURE !!! Every blue point is exactly equal to 0.

## Slide 16: B-spline summary
Piecewise polynomial defined on a sequence of knots
Smoothness depends on the degree and the number of basis functions
Estimate the parameters using the least squares formulation
Question: Can we use a high number of basis functions
and generate a smooth estimate??

## Slide 17: P-splines
Penalize 2nd order derivative to enforce smoothness
Eilers & Marx 1996: base penalty on 2nd order finite differences of adjacent
coefficients to enforce smoothness

## Slide 18: P-splines & PLS formulation

## Slide 19: Choosing
determines the effect of the smoothness penalty
We choose it based on the generalized cross-validation criterium GCV

## Slide 20: P-spline summary
Question: Can we use P-splines and introduce a priori domain knowledge??
Expand the B-spline formulation by a smoothness penalty based on the
2nd order finite differences of adjacent parameters
Penalized least squares formulation for parameter estimation
Choose optimal smoothness parameter based on GCV criterium

## Slide 21: Shape-constraint P-splines
Expand the idea of Eilers & Marx leading to P-splines by introducing
shape constraints of the form
The shape constraint matrix is consists of
  a mapping matrix based on finite differences of adjacent parameters
  a weighting matrix determining if the constraint is active
This leads to the following formulation
which can be solved iteratively given the algorithm on the next slide.
with

## Slide 23: Example Increasing Behaviour
Constraint formulation
Mapping matrix
Weighting matrix

## Slide 25: Various constraints
Through the choice of the mapping matrix and the weighting matrix various constraints can be incorporated

## Slide 26: Extension to higher dimensions 1
Tensor-product B-splines for 2d
  TP B-spline basis function
  TP B-spline basis
  TP B-spline basis matrix
  Least squares formulation
Notes: Row-wise Kronecker product
Constraints in different Dimensions

## Slide 27: Kronecker product

## Slide 28: Row-Wise Kronecker product

## Slide 29: Tensor-product P-spline
Penalize 2nd order derivative in both dimensions to enforce smoothness
Penalized Least Squares formulation
with the penalty matrix

## Slide 30: Tensor-product sC-P-spline
Constraints available for
  One dimension: e.g. increasing only in dimension 1
  Both dimensions: e.g increasing for dimension 1 and decreasing for dimension 2
Example: Increasing behavior in dimension 1

## Slide 31: Extension to higher dimensions 2
Additive models: from 2-d to -d without interaction terms
Modeling each function using a B-spline

## Slide 32: Extension to higher dimensions 3
Additive models: from 2-d to -d with interaction terms
Modeling each using a B-spline and each using a TP B-spline

## Slide 33: SC-P-splines Summary
Expand the P-spline formulation by using a priori domain knowledge via
shape constraints based on mapping matrices and weighting matrices
Iterative algorithm for parameter estimation
Choose constraint parameter based on your trust in the a
priori domain knowledge

## Slide 34: Experiment Heat Treatment process
Estimate the heat transfer coefficient based on measurements of
the temperature and the mass flow
A priori knowledge through the Nukiyama curve (peak)
Challenges
  Sparse Data
  Very noisy

## Slide 35: Data

## Slide 36: Best Model

## Slide 37: Experiment Hybrid modeling and Control
Estimate the differential current based on measurements of
the desired main valve position and the desired differential flow
Block diagram is given on the right
Challenges
  Discontinuous data

## Slide 38: Data

## Slide 39: Best Model
, with monotonicity for both dimensions

## Slide 40: summary
Linear models & theory for function approximation
Extension to nonlinear functions approximation using B-splines
Optimal smoothness using P-splines
Incorporation of a priori domain knowledge through shape-constraint P-splines
Multi-dim through additive models

## Slide 41: Thank you! Questions?
Jakob Weber